## Slide 1: Enabling Flexible Network FPGA Clusters in a Heterogeneous Cloud Data Center
Naif Tarafdar, Thomas Lin, Eric Fukuda,
Hadi Bannazadeh, Alberto Leon-Garcia, Paul Chow
University of Toronto

## Slide 2: Cloudy with a chance of FPGAs?
Big data needs more compute power: How about FPGAs in datacenters?
Datacenters are approximately 200 billion dollar industry
Datacenter applications are large
No large scale datacenter multi-FPGA fabric deployed until 2014

## Slide 3: Cloudy with a Chance of FPGAs?
Microsoft Catapult
  1632 Servers
  Bing search engine
  10 % more power, 95 % more throughput
Intel acquisition of Altera in December 2015
More than just a chance

## Slide 4: Large Clusters Difficult To Manage
Large resources of clusters difficult to manage
Expensive
Solution:
  Allow users framework to create their own clusters from a pool of available resources

## Slide 5: Related Work
Byma et al:
  FPGA broke into partial FPGAs
  Multiple users share portion of FPGA

## Slide 6: Related Work
Byma et al:
  FPGA broke into partial FPGAs
  Multiple users share portion of FPGA
IBM Supervessel:
  FPGA tightly coupled with virtual machine CPU
  Connected to CPU via shared memory
  Network connection through CPU

## Slide 7: Related Work
Byma et al:
  FPGA broke into partial FPGAs
  Multiple users share portion of FPGA
IBM Supervessel:
  FPGA tightly coupled with Virtual Machine CPU
  Connected to CPU via shared memory
  Network connection through CPU
Amazon:
  FPGA(s) tightly coupled with virtual machine CPU
  Up to 8 FPGAs connected via high performance network link

## Slide 8: Related Work
Byma et al:
  FPGA broke into partial FPGAs
  Multiple users share portion of FPGA
IBM Supervessel:
  FPGA tightly coupled with Virtual Machine CPU
  Connected to CPU via shared memory
  Network connection through CPU
Amazon:
  FPGA(s) tightly coupled with virtual machine CPU
  Up to 8 FPGAs connected via high performance network link
IBM Hyperscale
  Network connected FPGAs
  Modified Openstack to accept bitstream and then returns IP address and programmed FPGA to user

## Slide 9: Problems We Target
Large multi-FPGA systems
  Create abstraction between FPGAs in multi-FPGA systems
  Easy scalability of system

## Slide 10: Problems We Target
Large multi-FPGA systems
  Create abstraction between FPGAs in multi-FPGA systems
  Easy scalability of system
Network capabilities
  FPGA cluster directly accessible by any other network device in the datacenter

## Slide 11: Overall System View
FPGA Mapping File
Logical Cluster Description
FPGA Cluster Generator
User
Input From User

## Slide 12: Overall System View
FPGA Cluster Generator
User
Output to VM with FPGA Tools
Individual FPGA Projects

## Slide 13: Overall System View
FPGA Cluster Generator
User
Output to Cloud Manager
Command For Resource Allocation
Commands For Connecting FPGAs to Network

## Slide 14: Overall System View
FPGA Cluster Generator
User
Output To User
MAC addresses of FPGAs in Multi-FPGA Cluster

## Slide 15: Baseline Infrastructure
SAVI (Smart Applications on Virtualized Infrastructure)
OpenStack (Cloud Managing Software)
Xilinx SDAccel (FPGA Hypervisor)

## Slide 16: SAVI (Smart Applications on Virtualized Infrastructure)

## Slide 17: Cloud Managing Software: OpenStack

## Slide 18: FPGA Hypervisor: Xilinx SDAccel
Abstracts physical hardware on FPGA and provides software interface for these modules
Publicly available through Xilinx
No network interface

## Slide 19: Contributions
Non-network FPGA from cloud

## Slide 20: Contributions
Non-network FPGA from cloud
Networking infrastructure for FPGAs to communicate in heterogeneous network
  Modified FPGA hypervisor for networking support
  FPGAs MAC addresses, accessible by any network device in datacenter

## Slide 21: Contributions
Non-network FPGA from cloud
Networking infrastructure for FPGAs to communicate in heterogeneous network
  Modified FPGA hypervisor for networking support
  FPGAs MAC addresses, accessible by any network device in datacenter
FPGA cluster generator

## Slide 22: Non-network FPGA from Cloud
Deployment Flow
  User develops their application on a VM without an FPGA.
  Save VM snapshot
  Upload VM snapshot to OpenStack
  Create new VM with snapshot and FPGA

## Slide 23: FPGA Hypervisor: Networking Hypervisor
Customized shell with:
  PCIe module
  Off Chip Memory controller
  1 GB Ethernet
Note: No partial reconfiguration

## Slide 24: Logical Cluster Description
FPGA Mapping File | 
Kernel A | FPGA 1
Kernel B | FPGA 1
Kernel C | FPGA 2

## Slide 25: Physical Mapping

## Slide 26: I/O to FPGAs in Cluster
Input
Output

## Slide 27: Scaling Up the Clusters

## Slide 28: Networking Backend
OpenStack
SAVI Network Manager
FPGA Cluster Generator
Network Port Request

## Slide 29: Networking Backend
OpenStack
SAVI Network Manager
FPGA Cluster Generator
Network MAC address

## Slide 30: Networking Backend
OpenStack
SAVI Network Manager
FPGA Cluster Generator
Network MAC address
FPGA Port on Physical Switch

## Slide 31: Resource Utilization
Hardware Setup | LUTS | Flip-Flops | BRAM
SDAccel Base | 53346 (12.3 %) | 64550 (7.45 %) | 228 (15.5 %)
Ethernet Support | 8998 (2.1 %) | 11574 (1.34 %) | 0 (0 %)
Input Module | 169 (0.039 %) | 294 (0.033 %) | 2 (1.36 %)
Output Module | 773(0.178 %) | 402 (0.059%) | 4 (2.72 %)
Total Available | 233200 | 866400 | 1470

## Slide 32: Testing Latency and Throughput
Directly Connected CPU to FPGA
VM to one FPGA in SAVI

## Slide 33: Testing Latency and Throughput
VM to two FPGA chain in SAVI
VM to three FPGA chain in SAVI

## Slide 34: Round-trip Latency
Test | Latency (ms)
CPU + FPGA | 0.0650
VM + 1 FPGA | 0.500
VM + 2 FPGA | 0.645
VM + 3 FPGA | 0.790

## Slide 35: Round-trip Latency
CPU > VM
Extra network Hop
Test | Latency (ms)
CPU + FPGA | 0.0650
VM + 1 FPGA | 0.500
VM + 2 FPGA | 0.645
VM + 3 FPGA | 0.790

## Slide 36: Round-trip Latency
Linear
Test | Latency (ms)
CPU + FPGA | 0.0650
VM + 1 FPGA | 0.500
VM + 2 FPGA | 0.645
VM + 3 FPGA | 0.790

## Slide 37: Microbenchmark Throughput
Chart: Throughput (Mbits/second) of Microbenchmarks
| CPU + FPGA | VM + 1 FPGA | VM + 2 FPGA | VM + 3 FPGA | VM + VM | Internal FPGA B/W
 | 948 | 248 | 249 | 247 | 132 | 4000
Physical Limit of Network Link

## Slide 38: Microbenchmark Throughput
Chart: Throughput (Mbits/second) of Microbenchmarks
| CPU + FPGA | VM + 1 FPGA | VM + 2 FPGA | VM + 3 FPGA | VM + VM | Internal FPGA B/W
 | 948 | 248 | 249 | 247 | 132 | 4000
Physical Limit of Network Link

## Slide 39: Microbenchmark Throughput
Chart: Throughput (Mbits/second) of Microbenchmarks
| CPU + FPGA | VM + 1 FPGA | VM + 2 FPGA | VM + 3 FPGA | VM + VM | Internal FPGA B/W
 | 948 | 248 | 249 | 247 | 132 | 4000
Physical Limit of Network Link

## Slide 40: Microbenchmark Throughput
Physical Limit of Network Link
Chart: Throughput (Mbits/second) of Microbenchmarks
| CPU + FPGA | VM + 1 FPGA | VM + 2 FPGA | VM + 3 FPGA | VM + VM | Internal FPGA B/W
 | 948 | 248 | 249 | 247 | 132 | 4000

## Slide 41: Case Study: Scalability of Query Processing Engine
Representative Case study: Database Streaming Query Processing Engine
  Size
  Streaming
Scalable

## Slide 42: Case Study: Scalability of Query Processing Engine
Query Processing Engine

## Slide 43: Case Study: Scalability of Query Processing Engine
Query Processing Engine
Scheduler
Query Processing Engine

## Slide 44: Case Study: Scalability of Query Processing Engine
Query Processing Engine
Scheduler
Query Processing Engine
-Replicated 6 times
3 FPGAs
2 units /FPGA

## Slide 45: Case Study: Scalability of Query Processing Engine
Chart: Throughput (Mbits/Second) of Replications
 | 20 | 45 | 58 | 75 | 93 | 110

## Slide 46: Conclusion and Summary
Users can create elastic FPGA clusters from cloud easily
  Inter-FPGA fabric automatically generated
  FPGAs provided network interface
Little overhead
Easy to scale

## Slide 47: Future Work
Infrastructure Upgrade
  10G
  Partial Reconfiguration

## Slide 48: Future Work
Infrastructure Upgrade
  10G
  Partial Reconfiguration
Automatic Partitioning/Scheduling
  HLS Model (Scheduler): Behavioral
  Circuit Partitioning

## Slide 49: Future Work
Infrastructure Upgrade
  10G
  Partial Reconfiguration
Automatic Partitioning/Scheduling
  HLS Model (Scheduler): Behavioral
  Circuit Partitioning
Debugging of Large clusters
  Combine individual debug environments
  Monitor health

## Slide 50: Future Work
Infrastructure Upgrade
  10G
  Partial Reconfiguration
Automatic Partitioning/Scheduling
  HLS Model (Scheduler): Behavioral
  Circuit Partitioning
Debugging of Large clusters
  Combine individual debug environments
  Monitor health
Large Scale Applications
  Networking Applications (NFV)
  Distributed Applications (Web-search)
  Heterogeneous IOT Applications

## Slide 51: Thank You

## Slide 52: Questions?
Email: naif.tarafdar@mail.utoronto.ca