## Slide 1: A Modular Heterogeneous Stack for Deploying FPGAs and CPUs in the Data Center
Nariman Eskandari, Naif Tarafdar, Daniel Ly-Ma, Paul Chow
Notes: Hi, welcome to my talk on a modular heterogeneous stack for deploying fpgas and cpus in the data center.
I am naif Tarafdar and I will be presenting on behalf of Nariman eskandari who could not make it due to visa issues.

## Slide 2: FPGAs in Clouds and Data Centers?
Microsoft
  Catapult v1(2014)
    10% more power, 95% throughput
  Catapult v2 (2017)
    Brainwave (2017)
Notes: This is a question that has been quite definitively answered but do FPGAs belong in clouds and data centers.
Well in 2014 Microsoft has launched catapult v1 where at scale they deployed fpgas in their bing search engine and observed 95 % more throughput with only 10 % more power
They further continued targeting scalability in v2 by connecting fpgas directly on the network as abump on the wire
In 2014, Microsoft introduced the new servers that FPGAs are deployed in them.
By only 10% more power consumption, the servers almost double the performance of bing search engine.
3 years later it introduced catapult v2 that is a cloud infrastructure
And in the year they released the machine learning platform that is built on top of catapult v2 called brainwave

## Slide 3: FPGAs in Clouds and Data Centers?
Microsoft
  Catapult v1(2014)
    10% more power, 95% throughput
  Catapult v2 (2017)
    Brainwave (2017)
Amazon
  AWS F1(2017)
Notes: The popularity of FPGAs for scale applications can be seen as they are now also deployed in cloud compute services such as amazon f1.

## Slide 4: Background: Heterogeneous Communication
Architecture models for FPGA and CPU clusters:
CPU
FPGA
Network
CPU
FPGA
CPU
FPGA
CPU
FPGA
Peer Model
Slave Model
Network
Notes: Now that we have quickly gone over some motivation to show that heterogeneous devices belong in the data center, I’d like to cover some background.
Firstly I will cover communication models.
On the left hand side we have
As background I want to define some term
There are to models for architecture of CPUs and FPGAs
Slave model: that CPUs are connected to FPGAs through PCIe or other links but CPUs are connected to the network
So if a FPGA wants to send data to another FPGA it should go through cpus and network
In standalone model, FPGAs and CPUs are accessible though the network as standalone node

## Slide 5: Background: Heterogeneous Communication
Architecture models for FPGA and CPU clusters:
CPU
FPGA
Network
CPU
FPGA
CPU
FPGA
CPU
FPGA
Peer Model
Slave Model
Network
Notes: As background I want to define some term
There are to models for architecture of CPUs and FPGAs
Slave model: that CPUs are connected to FPGAs through PCIe or other links but CPUs are connected to the network
So if a FPGA wants to send data to another FPGA it should go through cpus and network
In standalone model, FPGAs and CPUs are accessible though the network as standalone node

## Slide 6: Background: Heterogeneous Communication
Architecture models for FPGA and CPU clusters:
CPU
FPGA
Network
CPU
FPGA
CPU
FPGA
CPU
FPGA
Peer Model
Slave Model
Network
Notes: As background I want to define some term
There are to models for architecture of CPUs and FPGAs
Slave model: that CPUs are connected to FPGAs through PCIe or other links but CPUs are connected to the network
So if a FPGA wants to send data to another FPGA it should go through cpus and network
In standalone model, FPGAs and CPUs are accessible though the network as standalone node

## Slide 7: Background: Heterogeneous Communication
Architecture models for FPGA and CPU clusters:
CPU
FPGA
Network
CPU
FPGA
CPU
FPGA
CPU
FPGA
Peer Model
Slave Model
Network
Notes: As background I want to define some term
There are to models for architecture of CPUs and FPGAs
Slave model: that CPUs are connected to FPGAs through PCIe or other links but CPUs are connected to the network
So if a FPGA wants to send data to another FPGA it should go through cpus and network
In standalone model, FPGAs and CPUs are accessible though the network as standalone node

## Slide 8: Background: Heterogeneous Communication
Architecture models for FPGA and CPU clusters:
CPU
FPGA
Network
CPU
FPGA
CPU
FPGA
CPU
FPGA
Peer Model
Slave Model
Network
Communication
  Peer model: No different way to communicate between Accelerators and CPUs
    Easier
    Direct connection between accelerators
Notes: As background I want to define some term
There are to models for architecture of CPUs and FPGAs
Slave model: that CPUs are connected to FPGAs through PCIe or other links but CPUs are connected to the network
So if a FPGA wants to send data to another FPGA it should go through cpus and network
In standalone model, FPGAs and CPUs are accessible though the network as standalone node

## Slide 9: Background: System Orchestration
Heterogeneous Cloud Provider
User
Request
User issues request
CPU
FPGA
Give user network handle of cluster
CPU
FPGA
Network
Resources connected on network
Network Handle of Cluster

## Slide 10: Contributions
Galapagos: Rearchitected work in [FPGA 2017] to focus on modularity
  Previously large monolithic layer
  Modularity allows users to experiment with design space for heterogeneous clusters
  Also addressed scalability issues in [FPGA 2017]
1 Naif Tarafdar et al. Enabling Flexible Network FPGA Clusters in a Heterogeneous Cloud Data Center, FPGA 2017.
Notes: Remove reliability to not explain, new architecture with a focus on modularity

## Slide 11: Contributions
Galapagos: Rearchitected work in [FPGA 2017] to focus on modularity
  Previously large monolithic layer
  Modularity allows users to experiment with design space for heterogeneous clusters
  Also addressed scalability issues in [FPGA 2017]
HUMboldt (Heterogeneous Uniform Messaging) : A Communication Layer
  Heterogeneous (multi-FPGA and CPU)
  Same high-level code for software and hardware (portable)
  Easy to use in order to make scalable applications for CPU/FPGA Cluster.
1 Naif Tarafdar et al. Enabling Flexible Network FPGA Clusters in a Heterogeneous Cloud Data Center, FPGA 2017.
Notes: Remove reliability to not explain, new architecture with a focus on modularity

## Slide 12: Outline
Galapagos
HUMboldt
Results
Conclusion
Future Work

## Slide 13: Outline
Galapagos
HUMboldt
Results
Conclusion
Future Work

## Slide 14: Heterogeneous Abstraction Stack
Monolithic Orchestration Layer
[FPGA 2017]
Notes: Animate, show modular contributions (animate show hum and Galapagos, and old monolithic)

## Slide 15: Heterogeneous Abstraction Stack
Galapagos
HUMboldt
Notes: Animate, show modular contributions (animate show hum and Galapagos, and old monolithic)

## Slide 16: Galapagos: Middleware Layer
VM
VM
VM
User can define a FPGA cluster using cluster description files and AXI-Stream kernels
Tool Flow
Network
Kernel
AXI-Stream
FPGA 2
FPGA 3
FPGA 1
Kernel
Kernel
AXI-Stream
File
Notes: Put numbers for FPGAs, talk about kernels when orchestrating!!

## Slide 17: Galapagos: Middleware Layer
VM
VM
VM
User can define a FPGA cluster using cluster description files and AXI-Stream kernels
Tool Flow
Network
Kernel
AXI-Stream
FPGA 2
FPGA 3
FPGA 1
Kernel
Kernel
AXI-Stream
File
Notes: Put numbers for FPGAs, talk about kernels when orchestrating!!

## Slide 18: Galapagos: Middleware Layer
VM
VM
VM
User can define a FPGA cluster using cluster description files and AXI-Stream kernels
Tool Flow
Network
Kernel
AXI-Stream
FPGA 2
FPGA 3
FPGA 1
Kernel
Kernel
AXI-Stream
File
Notes: Put numbers for FPGAs, talk about kernels when orchestrating!!

## Slide 19: Galapagos: Middleware Layer
VM
VM
VM
User can define a FPGA cluster using cluster description files and AXI-Stream kernels
Tool Flow
Network
Kernel
AXI-Stream
FPGA 2
FPGA 3
FPGA 1
Kernel
Kernel
AXI-Stream
File
Notes: Put numbers for FPGAs, talk about kernels when orchestrating!!

## Slide 20: Galapagos Hypervisor
The Hypervisor abstracts all the I/O interfaces
Limitations of the base infrastructure:
  Closed source (proprietary IPs)
  Not easily portable for other boards support (Heterogeneity)
PCIE
Driver
Network
2
x DDR
Application
Region
CPU
Notes: less Details!!!!!!!!!!
One slide for these three

## Slide 21: Galapagos Hypervisor
The Hypervisor abstracts all the I/O interfaces
Limitations of the base infrastructure:
  Closed source (proprietary IPs)
  Not easily portable for other boards support (Heterogeneity)
Redesigned using publicly available Xilinx IPs
Supports higher level of the network stack.
  IP layer
  Transport Layer (e.g. TCP)
PCIE
Driver
Network
2
x DDR
Application
Region
CPU
Notes: less Details!!!!!!!!!!
One slide for these three

## Slide 22: Galapagos Hypervisor
The Hypervisor abstracts all the I/O interfaces
Limitations of the base infrastructure:
  Closed source (proprietary IPs)
  Not easily portable for other boards support (Heterogeneity)
Redesigned using publicly available Xilinx IPs
Supports higher level of the network stack.
  IP layer
  Transport Layer (e.g. TCP)
FPG
FPGA
PCIE
Driver
Network
2
x DDR
Application
Region
CPU
Notes: less Details!!!!!!!!!!
One slide for these three

## Slide 23: Galapagos: Hypervisor Application Region
[FPGA 2017]
Galapagos
Notes: Slide number? Highlight, Scalability and Modularity Improvements for Galapagos, Show box of app region in shell, remove all base infrastructe, vsn 1,

## Slide 24: Galapagos: Hypervisor Application Region
[FPGA 2017]
Galapagos
Notes: Slide number? Highlight, Scalability and Modularity Improvements for Galapagos, Show box of app region in shell, remove all base infrastructe, vsn 1,

## Slide 25: Galapagos: Application Region – Router
[FPGA 2017]
Galapagos
Notes: First animate around app region, remove and continue

## Slide 26: Galapagos: Application Region – Network Bridge
[FPGA 2017]
Galapagos
Notes: Moving laser pointer a lot over figures. Point to one, then talk and move on, just talk with animation rather than depending on laser

## Slide 27: Galapagos: Application Region – Comm Bridge
[FPGA 2017]
Galapagos
Notes: Delete that
Have a summery of Galapagos
Why we transit to HUMbolt

## Slide 28: Outline
Base infrastructure
Galapagos
HUMboldt
Results
Conclusion
Future Work

## Slide 29: HUMboldt (Heterogeneous Uniform Messaging) Communication Layer
A message passing communication layer
A minimal subset of MPI
  Only blocking send and receives
Software and Hardware library
  Exact same source code for both hardware and software
  Functional portability
Notes: Mention HUMboldt name earlier and define it, same source code works for both hw/sw

## Slide 30: HUMboldt Hardware
All the functions are implemented as High-Level Synthesis (HLS) functions
  Library for user to integrate in HLS code
  Functional portability
  Easy to use
The underlying protocol is handled by Galapagos
Notes: Mention HLS library,
Show animation of on chip and off chip. Box highlighting the fact that they are all on one fpga

## Slide 31: HUMboldt Software
Uses standard socket programming libraries
  TCP and Ethernet
Software kernels communicating through a mature software MPI library (MPICH)
It parses the cluster description files at runtime to choose the right protocol
  Hardware node: HUMboldt
  Software nodes: MPICH
Notes: A figure for sw to sw

## Slide 32: System Tool Flow
HUMboldt has two branches for creating the entire cluster
  Software kernels
  Hardware kernels
Same code can be used for both software and hardware kernels
Notes: Box here is necessary
Hard to follow
Change hardware library to HUMboldt!
MPICH

## Slide 33: System Tool Flow
HUMboldt has two branches for creating the entire cluster
  Software kernels
  Hardware kernels
Same code can be used for both software and hardware kernels
Notes: Box here is necessary
Hard to follow
Change hardware library to HUMboldt!
MPICH

## Slide 34: System Tool Flow
HUMboldt has two branches for creating the entire cluster
  Software kernels
  Hardware kernels
Same code can be used for both software and hardware kernels
Notes: Box here is necessary
Hard to follow
Change hardware library to HUMboldt!
MPICH

## Slide 35: System Tool Flow
Ease of use
  Changing the underlying protocol
<cluster>
<node>
<type> sw </type>
<kernel> 0 </kernel>
<mac_addr> ac:c4:7a:88:c0:47 </mac_addr>
<ip_addr> 10.1.2.152 </ip_addr>
</node>
<node>
<appBridge>
<name> Humboldt_bridge</name>
</appBridge>
<board> adm-8k5-debug </board>
<type> hw </type>
<comm> eth </comm>
<kernel> 1 </kernel>
.
.
.
<kernel> 16 </kernel>
<mac_addr> fa:16:3e:55:ca:02 </mac_addr>
<ip_addr> 10.1.2.101 </ip_addr>
</node>
</cluster>
Notes: Spend less time
HUMboldt bridge
Cluster Description File )title)
Change red on black, include text and make it easier to read

## Slide 36: System Tool Flow
Ease of use
  Changing the underlying protocol
  Changing from software to hardware
<cluster>
<node>
<type> sw </type>
<kernel> 0 </kernel>
<mac_addr> ac:c4:7a:88:c0:47 </mac_addr>
<ip_addr> 10.1.2.152 </ip_addr>
</node>
<node>
<appBridge>
<name> Humboldt_bridge</name>
</appBridge>
<board> adm-8k5-debug </board>
<type> hw </type>
<comm> eth </comm>
<kernel> 1 </kernel>
.
.
.
<kernel> 16 </kernel>
<mac_addr> fa:16:3e:55:ca:02 </mac_addr>
<ip_addr> 10.1.2.101 </ip_addr>
</node>
</cluster>
Notes: Spend less time
HUMboldt bridge
Cluster Description File )title)
Change red on black, include text and make it easier to read

## Slide 37: Outline
Goals
Contributions
Previous Works
Galapagos
HUMboldt
Results
Conclusion
Future Work

## Slide 38: Results: Testbed
The testbed that is used is a cluster of:
  Intel Xeon E5-2650 (2.20 GHz)
  12 physical core, 24 threads
Alpha Data ADM-PCIE-8k5
  Xilinx KU115 UltraScale devices
Notes: Bullet point
Instead of part number just mention family
Be specific when mentioninc CPU cores

## Slide 39: Galapagos/HUMboldt Resource Utilization
Abstraction Layer IP | LUTs | Flip-Flops | BRAMs
I) Hypervisor | 14.4 % | 9.1 % | 11.8 %
II) Network Bridge TCP | 4.4 % | 2.4 % | 0.1 %
III) Network Bridge Ethernet | 0.1 % | 0.1 % | 0.1 %
IV) HUMboldt Bridge | 0.1 % | 0.1% | 0.05 %
V) Router | 0.8 % | 0.5 % | 0.05 %
Total TCP (1 + II + IV + V) | 19.7 % | 12.1 % | 15.9 %
Total Ethernet (1 + III + IV + V) | 15.3 % | 9.7 % | 12.0 %
Notes: Fix second point (table?) mention what resource. LUTS

## Slide 40: Galapagos/HUMboldt Resource Utilization
Abstraction Layer IP | LUTs | Flip-Flops | BRAMs
I) Hypervisor | 14.4 % | 9.1 % | 11.8 %
II) Network Bridge TCP | 4.4 % | 2.4 % | 0.1 %
III) Network Bridge Ethernet | 0.1 % | 0.1 % | 0.1 %
IV) HUMboldt Bridge | 0.1 % | 0.1% | 0.05 %
V) Router | 0.8 % | 0.5 % | 0.05 %
Total TCP (1 + II + IV + V) | 19.7 % | 12.1 % | 15.9 %
Total Ethernet (1 + III + IV + V) | 15.3 % | 9.7 % | 12.0 %
Notes: Fix second point (table?) mention what resource. LUTS

## Slide 41: Galapagos/HUMboldt Resource Utilization
Abstraction Layer IP | LUTs | Flip-Flops | BRAMs
I) Hypervisor | 14.4 % | 9.1 % | 11.8 %
II) Network Bridge TCP | 4.4 % | 2.4 % | 0.1 %
III) Network Bridge Ethernet | 0.1 % | 0.1 % | 0.1 %
IV) HUMboldt Bridge | 0.1 % | 0.1% | 0.05 %
V) Router | 0.8 % | 0.5 % | 0.05 %
Total TCP (1 + II + IV + V) | 19.7 % | 12.1 % | 12.9 %
Total Ethernet (1 + III + IV + V) | 15.3 % | 9.7 % | 12.0 %
Notes: Fix second point (table?) mention what resource. LUTS

## Slide 42: Galapagos/HUMboldt Resource Utilization
Abstraction Layer IP | LUTs | Flip-Flops | BRAMs
I) Hypervisor | 14.4 % | 9.1 % | 11.8 %
II) Network Bridge TCP | 4.4 % | 2.4 % | 0.1 %
III) Network Bridge Ethernet | 0.1 % | 0.1 % | 0.1 %
IV) HUMboldt Bridge | 0.1 % | 0.1% | 0.05 %
V) Router | 0.8 % | 0.5 % | 0.05 %
Total TCP (1 + II + IV + V) | 19.7 % | 12.1 % | 15.9 %
Total Ethernet (1 + III + IV + V) | 15.3 % | 9.7 % | 12.0 %
Notes: Fix second point (table?) mention what resource. LUTS

## Slide 43: Galapagos/HUMboldt Resource Utilization
Abstraction Layer IP | LUTs | Flip-Flops | BRAMs
I) Hypervisor | 14.4 % | 9.1 % | 11.8 %
II) Network Bridge TCP | 4.4 % | 2.4 % | 0.1 %
III) Network Bridge Ethernet | 0.1 % | 0.1 % | 0.1 %
IV) HUMboldt Bridge | 0.1 % | 0.1% | 0.05 %
V) Router | 0.8 % | 0.5 % | 0.05 %
Total TCP (1 + II + IV + V) | 19.7 % | 12.1 % | 15.9 %
Total Ethernet (1 + III + IV + V) | 15.3 % | 9.7 % | 12.0 %
Notes: Fix second point (table?) mention what resource. LUTS

## Slide 44: Results: Microbenchmarks
Hardware Kernel
FPGA
Hardware Kernel
Hardware Kernel
FPGA
Hardware Kernel
FPGA
Software Kernel
CPU
Hardware Kernel
FPGA
Hardware Kernel
FPGA
Software Kernel
CPU
Software Kernel
CPU
Software Kernel
CPU
MPICH
HUMboldt
HUMboldt
HUMboldt
HUMboldt
Notes: MPICH last row, investigate colour schemes

## Slide 45: Results: Throughput
Ethernet
Notes: Gap draw an arrow
Where the limit is for TCP

## Slide 46: Results: Throughput
Ethernet
Notes: Gap draw an arrow
Where the limit is for TCP
Highlight we are not the bottleneck (animate point?)

## Slide 47: Results: Throughput
TCP
Notes: Gap draw an arrow
Where the limit is for TCP

## Slide 48: Results: Throughput
TCP
Notes: Gap draw an arrow
Where the limit is for TCP

## Slide 49: Results: Latency
Microbenchmarks | Ethernet (µs) | TCP (µs)
Hardware to Hardware (same node) | 0.2 | 0.2
Hardware to hardware (different node) | 5.7 | 15.2
Software to Hardware | 27.5 | 48.8
Hardware to Software | 34.7 | 113.6
Zero-payload packets
Relevant Comparison: Microsoft Catapult V2
  40 G Ethernet
  Lightweight transport layer
  2.88 µs round trip
Notes: Same node, no network

## Slide 50: Results: Latency
Microbenchmarks | Ethernet (µs) | TCP (µs)
Hardware to Hardware (same node) | 0.2 | 0.2
Hardware to hardware (different node) | 5.7 | 15.2
Software to Hardware | 27.5 | 48.8
Hardware to Software | 34.7 | 113.6
Zero-payload packets
Relevant Comparison: Microsoft Catapult V2
  40 G Ethernet
  Lightweight transport layer
  2.88 µs round trip
Notes: Comparable round trip latency as Humboldt sends 4 packets instead of 2

## Slide 51: Results: Latency
Microbenchmarks | Ethernet (µs) | TCP (µs)
Hardware to Hardware (same node) | 0.2 | 0.2
Hardware to hardware (different node) | 5.7 | 15.2
Software to Hardware | 27.5 | 48.8
Hardware to Software | 34.7 | 113.6
Zero-payload packets
Relevant Comparison: Microsoft Catapult V2
  40 G Ethernet
  Lightweight transport layer
  2.88 µs round trip
Notes: Software a lot slower

## Slide 52: Outline
Goals
Contributions
Previous Works
Galapagos
HUMboldt
Results
Conclusion
Future Work

## Slide 53: Conclusion
Galapagos: the improved version of the base infrastructure which is more modular, scalable, and reliable.
HUMboldt: a communication layer that is:
  Heterogeneous: different nodes can talk in a same language
  Functional portable: same code can be used for both software and hardware
Abstraction layers can with very minimal overhead improve scalability, modularity and productivity.
Notes: Conclusion and summary not just conclusion
Layering! – abstraction overhead minimal but easier to use

## Slide 54: Outline
Goals
Contributions
Previous Works
Hypervisor
Application Region
HUMboldt
Tool Flow
Results
Conclusion
Future Work

## Slide 55: Future Work
Application that shows the true power of HUMboldt and Galapagos.
Investigate other layers of abstraction.
Implementing another type of communication layer.
  Streaming model
Notes: Different abstractions, remove mpi stuff,

## Slide 56: Acknowledgements

## Slide 57
Thank you
Questions?
Email: naif.tarafdar@mail.utoronto.ca
Notes: Put email, and repos, move repos to uofthprc, add acknowledgements, Xilinx , Huawei, nserc, cmc

## Slide 58: Back Up Slides

## Slide 59: Base Infrastructure: System Interface
The base infrastructure takes three files to create a cluster.
  Logical file
  Mapping file
  MAC address file

## Slide 60: Base Infrastructure: System Interface
Logical file
Mapping file
MAC address file

## Slide 61: Galapagos: Logical file
Base infrastructure Logical file
Galapagos Logical file

## Slide 62: Galapagos: Mapping File
Base infrastructure Mapping file
Galapagos Mapping file

## Slide 63: HUMboldt Sample code
To make HUMboldt code Synthesizable
  Change ”main” to hardware core name
  Rank connects to id port that is defined in logical file
  Size is a constant that is defined in logical file
  And the HLS pragmas should be added

## Slide 64: Base Infrastructure: Application Region
Base Infrastructure connects all the Streaming IPs automatically using the Cluster description files.
  Logical file
  Mapping file
  MAC address file

## Slide 65: Galapagos: TCP Network Bridge
Reliable connections
Server as the receiver
  Opens and listens to a specific port
  Accepts the connections and stores the session ID into the session table
  Receives data from session and forward them as AXI-Stream packets.
Client as sender
  Creates the connection to server if it is not made
  Stores the session ID into the session table
  Send data out to the other network nodes

## Slide 66: Resource Utilization
The resource utilization is 20% when the user chooses TCP
It is 15% when the user chooses Ethernet
Results are based on the 8K5 board

## Slide 67: FPGAs in Clouds and Data Centers?
Catapult v1(2014)
  Acceleration of Bing search engine
  10% more power, 95% more throughput
Catapult v2 (2017)
  Cloud based infrastructure
Notes: Remove the detail
List of many people

## Slide 68: Base Infrastructure Application Region
Notes: Showing packet is good
Make it more clear for a packet

## Slide 69: Base Infrastructure Application Region
Notes: Showing packet is good
Make it more clear for a packet

## Slide 70: Base Infrastructure Application Region
FPGA 2
FPGA 1
Application Region
Application Region
3
4
Notes: The switch os conectefd in the cluster whather in same or differetn
Same fpga dicrect connection
Diffent fpga go through packet formatter
Pf: Adds a network header

## Slide 71: Galapagos: Application Region
Adding Router to address scalability limitation

## Slide 72: Galapagos Application Region
FPGA 2
FPGA 1
Application Region
Application Region
3
4
Notes: The implementation of application layer or communication layer is independent from network protocol
For example
MPI as communication not related to what is the type of network brge

## Slide 73: Galapagos: Network Bridge
Receives the packets from network and check if they are for this FPGA
Sends the outgoing packets out with a destination MAC or IP address
Interfaces are consistent with Galapagos
Notes: Too small

## Slide 74: Base Infrastructure Application Region
FPGA 2
FPGA 1
Application Region
Application Region
3
4
Notes: The switch os conectefd in the cluster whather in same or differetn
Same fpga dicrect connection
Diffent fpga go through packet formatter
Pf: Adds a network header

## Slide 75: Base Infrastructure Application Region
Limitations:
  16 kernels in entire cluster
  Unreliable communications
  Not modular
FPGA
Application Region